## Slide 1
Temperature-Dependent SOC Estimation Using Deep Learning Models

## Slide 2
SOC
01
Objective & Goals
02
Introduction
03
Data Description
04
Methodology
05
Results and Analysis
OVERVIEW

## Slide 3
Objectives
Evaluate SOC estimation accuracy for Li-ion batteries at varying temperatures (0°C, 10°C, 25°C, 40°C) using LSTM, TCN, and Bi-LSTM models.
Compare model performance using RMSE to identify the most effective approach for temperature-dependent SOC estimation.
Goals
Train LSTM, TCN, and Bi-LSTM models for SOC estimation with optimized parameters.
Analyze SOC prediction accuracy across different operating temperatures.
Compare model strengths and weaknesses in various temperature scenarios.
Highlight real-world implications and propose future enhancements for improved SOC estimation.

## Slide 4
SOC
INTRODUCTION
Importance of SOC Estimation for Evs
State of Charge (SOC) is a critical metric for monitoring the health and performance of lithium-ion batteries in electric vehicles (EVs).
Accurate SOC estimation ensures efficient battery utilization, prolongs battery lifespan, and enhances vehicle safety by avoiding overcharging or deep discharging.
SOC estimation is particularly challenging in dynamic operating conditions, where temperature significantly influences battery performance.
Challenges of Temperature Variations
Temperature fluctuations (from 0°C to 40°C) directly affect:
  Battery capacity and internal resistance.
  Chemical reactions, leading to changes in voltage and current.
  SOC estimation accuracy, as models must adapt to these non-linear variations.
Low temperatures (e.g., 0°C) reduce battery efficiency, while higher temperatures can accelerate degradation, making robust estimation models essential.

## Slide 5
Overview of Modeling Approaches
LSTM (Long Short-Term Memory):
  Designed to handle sequential data with long-term dependencies.
  Ideal for capturing the complex temporal relationships in battery voltage, current, and temperature data.
  Features a memory cell to retain information over long periods, mitigating vanishing gradient issues seen in traditional RNNs.
TCN (Temporal Convolutional Network):
  Uses causal convolutions to model sequence data, ensuring predictions depend only on past inputs.
  Handles long-range dependencies efficiently through dilated convolutions.
  Robust to time-series variations, making it suitable for data with varying time scales (e.g., SOC at different temperatures).
Bi-LSTM (Bidirectional LSTM):
  Extends LSTM by processing the sequence in both forward and backward directions.
  Captures contextual information from both past and future inputs.
  Useful for applications requiring a deeper understanding of dependencies in the data, such as SOC influenced by sudden load or temperature changes.

## Slide 6
Data Description PART 1
Source: The dataset is recorded from Li-ion batteries under controlled laboratory conditions, simulating real-world
EV operations. It includes diverse operational scenarios such as varying discharge rates, load conditions, and
environmental temperatures.
Features:
Voltage (V): Represents the electrical potential difference across the battery terminals.
Current (I): Measures the flow of electric charge.
Temperature (T): Monitors the operating temperature, critical due to its impact on battery behavior.
SOC: The percentage of the battery’s capacity remaining, the target variable for prediction.
Target Variable:
State-of-Charge (SOC): Represents the battery's energy status, calculated using a combination of
Coulomb counting and voltage-based methods.
Data Collection Conditions:
Battery cycling data was collected at 0°C, 10°C, 25°C, and 40°C to evaluate temperature-induced variations
in performance.
Controlled experiments ensure consistency and reliability of the data.
Dataset Overview

## Slide 7
Data Description PART 2
Data Collection
Temperature Conditions
Recorded at: 0°C, 10°C, 25°C, and 40°C.
Relevance:
  Low temperatures (e.g., 0°C) increase internal resistance, reducing capacity.
  High temperatures (e.g., 40°C) accelerate chemical reactions, causing degradation.
In the Program: Data is segmented by temperature to evaluate SOC estimation performance under varying conditions.
Operational Conditions
Charge/Discharge Cycles: Simulate realistic EV usage patterns.
Relevance:
  EV batteries operate dynamically; accurate SOC estimation is essential for all scenarios.
In the Program: Models are trained on varied cycles, enhancing robustness for real-world applications.
Measured Parameters (Input Features)
Inputs: Voltage (V), Current (I), Temperature (T).
Relevance: These parameters influence SOC and are key for modeling battery behavior.
In the Program: Features are normalized and fed into sequential models (LSTM, TCN) for training.
Data Sampling and Recording
Relevance: Regular sampling ensures uniformity and captures temporal patterns.
In the Program: Sequential data is processed using the sliding window method to create time-series inputs.

## Slide 8
Methodology - Model
Model Architectures
LSTM (Long Short-Term Memory):
Sequential Learning: LSTM captures patterns in time-series data using memory cells and hidden states, which retain information over long sequences.
Relevance to SOC: As SOC estimation relies on past charge/discharge data, LSTM can effectively model these dependencies.
TCN (Temporal Convolutional Network):
Causal Convolutions: Ensures that predictions at time 𝑡 depend only on inputs from time 𝑡 and earlier, preserving temporal causality.
Dilated Convolutions: Uses increasing dilation rates to capture long-range dependencies without requiring large convolutional kernels, making it computationally efficient.
Relevance to SOC: TCN excels in handling sequential data with varying time scales, ideal for SOC estimation under dynamic conditions.
Bi-LSTM (Bidirectional LSTM):
Bidirectional Processing: Processes sequences in both forward and backward directions, leveraging past and future
data for improved context.
Relevance to SOC: Provides enhanced accuracy for tasks where future data can help infer present conditions, such as charge/discharge trends.

## Slide 9
Methodology - Training Setup
Training Parameters
Hyperparameters:
Batch Size: Affects training stability and speed. Smaller sizes (32) are used for TCN to match its lightweight architecture, while LSTM/Bi-LSTM uses 64 for better gradient updates.
Optimizers:
  Adam: Adaptive optimizer suitable for complex models like LSTM and Bi-LSTM, ensuring faster convergence.
  SGD: Simpler optimizer effective for TCN and smaller datasets but may require more epochs to converge.
Learning Rate: A fixed starting value of 0.001 with decay schedules for fine-tuning as training progresses.
Epochs: Set to 200 to ensure sufficient training cycles for convergence.
Loss Function: Mean Squared Error (MSE) minimizes the difference between predicted and actual SOC values.
Validation Strategy:
K-Fold Cross-Validation: Splits the dataset into 5 parts, using 4 for training and 1 for testing iteratively. This ensures robust evaluation by averaging performance across folds.
Comparison Strategy:
Models are trained for each temperature condition (0°C, 10°C, 25°C, 40°C) to evaluate how well they perform under varying conditions.
RMSE (Root Mean Square Error): Chosen as the evaluation metric to measure prediction accuracy, with lower RMSE indicating better performance.

## Slide 10
Model Comparison LSTM
Strengths
Weaknesses
Observations
Excellent at capturing long-term dependencies in sequential data, which is critical for SOC estimation.
Sequential processing makes training slower compared to parallel models like TCN
Performs reliably under normal conditions but struggles to maintain accuracy in extreme temperature ranges.

## Slide 11
Model Comparison Bi-LSTM
Strengths
Weaknesses
Observations
Processes input in both forward and backward directions, enhancing accuracy by capturing bidirectional temporal dependencies.
Higher computational cost due to processing the sequence twice (forward and backward).
Outperforms LSTM in dynamic conditions but lacks the speed advantage of convolutional models.

## Slide 12
Model Comparison TCN
Strengths
Weaknesses
Observations
Fast training with parallel processing and effective handling of long-range dependencies using dilated convolutions.
Lacks the bidirectional capabilities of Bi-LSTM, limiting contextual understanding in certain conditions.
Performs well across all temperatures but slightly trails Bi-LSTM in extreme conditions.

## Slide 13
Results and Analysis
Deep Learning Insights
LSTM:
Handles temporal sequences well.
Performance declines in extreme temperatures due to limited bidirectional learning.
RMSE: ~2.2% at 0°C.
Bi-LSTM:
Processes forward and backward temporal dependencies, improving accuracy.
Performs better in dynamic conditions compared to LSTM.
RMSE: ~1.91% at 0°C.
TCN:
Parallel processing with dilated convolutions enhances training speed and long-term dependency handling.
Best standalone performance across all temperatures.
RMSE: ~1.83% at 0°C.
TCN-BiLSTM:
Combines strengths of TCN and Bi-LSTM.
Superior SOC estimation accuracy under challenging conditions.
RMSE: ~1.70% at 0°C.

## Slide 14
Results and Analysis -Contd
Key Observations:
TCN and its hybrid models outperformed LSTM and Bi-LSTM, particularly at extreme temperatures (0°C and 40°C).
TCN-BiLSTM demonstrated the best overall performance due to its ability to capture long-term dependencies and bidirectional relationships.
Training Efficiency:
TCN was faster than LSTM and Bi-LSTM, reducing training time by approximately 30%.

## Slide 15
Conclusion and Future Work
Conclusion
Best Model: TCN-Bi-LSTM delivers the most accurate and robust SOC estimations by combining TCN’s speed and Bi-LSTM’s bidirectional temporal learning.
Key Insights:
Hybrid models outperform standalone models, ensuring reliable performance across temperatures.
Accurate SOC estimation improves EV performance, safety, and battery lifespan.
Future Work
Real-World Deployment: Optimize models for real-time onboard EV systems considering computational constraints.
Dataset & Testing: Expand datasets to include diverse scenarios like aging effects and dynamic load conditions.
Energy Efficiency: Develop lightweight versions of hybrid models for embedded systems.
System Integration: Combine SOC estimation with SOH prediction and thermal management for comprehensive EV solutions.